## Slide 1
Cache and Data Coherency
Tony He
2021-10

## Slide 2
What is cache？
Cache problems
Cache maintenance
目 录
CONTENTS

## Slide 3
What is cache?
01

## Slide 4: Cache Memory
CPU
CACHE
MAIN MEMORY
Word transfer
Block transfer
Cache的主要构成
  Cache 存储体
  地址转换单元
  替换单元

## Slide 5
Cortex A53 Cluster
Snoop Control Unit
Level 2 Cache
AMBA4 ACE MasterBus Interface
Core 1
L1 caches
Core 2
L1 caches
Core 3
L1 caches
Core 4
L1 caches

## Slide 6
External memory
Core
L1/L2 caches
Peripheral
DMA
New data generated
Clean
Got new data
0xffff_1234
Coherence
Carry
External memory
Core
L1/L2 caches
Peripheral
DMA
New data generated
Invalidate
Got new data
0xffff_1234
Coherence
Carry

## Slide 7
External Memory
Cache Line
Core 1
Register
New data generated
Core 2
Register
New data generated
Cache Line
x
x
y
y

## Slide 8: Cache Terminology
Hit vs Miss.
Eviction vs Linefill.
Clean vs Dirty.
Cacheability attributes.
  Non-cacheable.
  Write-back cacheable.
  Write-through cacheable.
Cache allocation hints.
  Read-Allocate, Transient Read-Allocate, or no Read-Allocate.
  Write-Allocate, Transient Write-Allocate, or no Write-Allocate.
Read allocate mode.
  i.e. memset().

## Slide 9: Associative Mapped Cache（全相联）
所有内存块都能映射进任意的缓存块。
命中率较高，缓存存储空间利用效率高。
速度低，成本高。
Tag
Offset
Address
B0
B1
……
L0
L1
L2
L3
Bn-1
Cache
Memory
Tag, Valid, Data

## Slide 10: Direct Mapped Cache（直相联）
所有主存块只能存入缓存中特定的位置（块号相同）。
硬件实现简单，成本低。
替换操作频繁，命中率低。
Tag
Index
Offset
Address
Memory
B0
B1
B2
B3
B4
B5
B6
B7
B8
B9
B10
B11
B12
B13
B14
L0
L1
L2
L3
B15
Cache
Group0
Group1
Group2
Group3
Tag, Valid, Data

## Slide 11: 组相联）
组间直相联，组内全相联。
  组号相等。
  组内各块任意存放。
块的冲突概率比较低，块利用率大幅度提高，块失效率明显降低。
实现难度和成本较高。
Tag
Set
Offset
Address
B0
B1
B2
B3
B4
B5
B6
B7
B8
B9
B10
B11
B12
B13
B14
L0
L1
L2
L3
B15
Cache
Memory
S0
S1
2-way set assoc. cache
From internet

## Slide 12: Typical Arm CPU Cache Info.
CPU | LSZ (Byte) | L1I | L1D | L2
A9 | 32 | 4-way set assoc. | 4-way set assoc. | 8/16-way set assoc.
A53 | 64 | 2-way set assoc. | 4-way set assoc. | 16-way set assoc. up to 2MB
M55 | 32 | 2-way set assoc. | 4-way set alloc | O
Instruction cache
  Read-Allocate.
Data cache and unified cache
  Read-Allocate, Write-Allocate.
  Write-Back, Write-Through.
  Transient hints.

## Slide 13
Cache problems
02

## Slide 14: Coherency Problems Caused by Cache
An update to a memory location by a CPU that accesses a cache might not be visible to other observers that can access memory.
Updates to memory locations by other observers that can access memory might not be visible to a CPU that accesses a cache.
Explicit cache maintenance is required to overcome the cache coherency problems above.

## Slide 15: Example scenarios for Cache Maintenance
Memory accessed by CPU and non-coherent DMA.
Self-modifying software.
Asymmetric shared memory.
  Sec vs NS, cacheable vs non-cacheable.
Changing security attribution of an address.
CPU
CACHE
MAIN MEMORY
Driver
Output
Input
Output
Output
Input
Input

## Slide 16
Cache maintenance
03

## Slide 17: Cache Maintenance
Operations (by set/way/VA)
Point of operation
Use of Memory Barriers
Clean
Invalidate
Clean and invalidate (flush)
Point of Unification (PoU).
  Coherent at CPU level, i.e., icache, dcache, TLB
Point of Coherency (PoC).
  Coherent at system level.
DMB
DSB
ISB
- Risk of stall data!?
- Risk of data loss!?

## Slide 18: Operations by VA
Clean/invalidate/flush(va, len).
  start = ROUND_DOWN(va, LSZ).
  end = ROUND_UP(va + len, LSZ).
len
LSZ
va
target memory
operating memory
range
start
end

## Slide 19: Cache Maintenance – Full lines
Input Memory
Output Memory
Inout Memory
write(va, len)
clean(va, len)
consume(va, len)
produce(va, len)
invalidate(va, len)
read(va, len)
write(va, len)
clean(va, len)
con_and_prod(va, len)
invalidate(va, len)
read(va, len)
LSZ
len
va

## Slide 20: Cache Maintenance – Incomplete lines
Input Memory
Output Memory
Inout Memory
Seqs
  write(va, len)
  clean(va, len)
  consume(va, len)
Risks
  Data loss risk if oth portion is used by other observers in parallel.
Seqs
  flush(va, len)
  produce(va, len)
  invalidate(va, len) or flush(va, len)
  read(va, len)
Risks
  What if CPU modifying oth after step#1?
  Stall data if use flush in step#3, or data loss if invalidate.
Seqs
  write(va, len)
  flush(va, len)
  con_and_prod(va, len)
  invalidate(va, len) or flush(va, len)
  read(va, len)
Risks
  See input and output memory cases.
va
oth
oth
len

## Slide 21: Data Coherency Issue – Mitigations
Not cache line aligned cases
Assumption.
  Incomplete cache line appears at the header and/or tail of the buffer only.
Copy input data from incomplete blocks to intermediate buffer.
  Each intermediate buffer shall occupy one complete cache line, i.e., obtained via osal_malloc_aligned().
  Skip copying if output buffer.
Produce output data to intermediate buffer plus provided complete block buffers.
Copy output data from intermediate buffer to incomplete blocks.
va
I2
oth
oth
len
I1
I3
I2
I1
I3
O2
O1
O3
O2
oth
len
O1
O3
oth
va
Copy-in
Produce
Copy-out

## Slide 22: Scenario: use stack/struct memory for DMA output
merak_driver/cipher/xts.c
merak_driver/drv/drv_hash.c
ce_lite/src/ce_hash.c
The output buffer MUST exclusively occupy one or more cache lines.

## Slide 23: Scenario: use scatter gather DMA buffer
Driver just needs to handle the start and end mis-aligned cases for memory coherency consideration, while assuming the middle entries shall be full page or exclusive buffer.
…
Blk0
Blkn
Blkn-1
page
page
page
page
ofs
len0
lenn